## Slide 1: Arduino Board
The Arduino project started at the Interaction Design Institute Ivrea (IDII) in Ivrea, Italy.The Wiring platform consisted of a printed circuit board (PCB) with an ATmega168 microcontroller, an IDE based on Processing and library functions to easily program the microcontroller. In 2003, Massimo Banzi, with David Mellis, another IDII student, and David Cuartielles, added support for the cheaper ATmega8 microcontroller to Wiring. But instead of continuing the work on Wiring, they forked the project and renamed it Arduino.

## Slide 2: Arduino…
is the go-to gear for artists, hobbyists, students, and anyone with a gadgetry dream.
rose out of another formidable challenge: how to teach students to create electronics, fast.
http://spectrum.ieee.org/geek-life/hands-on/the-making-of-arduino

## Slide 3: Getting Started
Check out: http://arduino.cc/en/Guide/HomePage
  Download & install the Arduino environment (IDE)
  Connect the board to your computer via the USB cable
  If needed, install the drivers
  Launch the Arduino IDE
  Select your board
  Select your serial port
  Open the blink example
  Upload the program

## Slide 4
Analog INPUTS
Digital I\O
PWM(3, 5, 6, 9, 10, 11)
PWR IN
USB
(to Computer)
SCL\SDA
(I2C Bus)
POWER
5V / 3.3V / GND
RESET
Notes: Look up analog ref

## Slide 5: Prototyping Circuits Solderless Breadboard
One of the most useful tools in an engineer or Maker’s toolkit. The three most important things:
  A breadboard is easier than soldering
  A lot of those little holes are connected, which ones?
  Sometimes breadboards break

## Slide 6: What’s a Breadboard?

## Slide 7: Solderless Breadboard
Each row (horiz.) of 5 holes are connected.
Vertical columns – called power bus are connected vertically

## Slide 8: Concepts: INPUT vs. OUTPUT
Referenced from the perspective of the microcontroller (electrical board).
Inputs is a signal / information going into the board.
Output is any signal exiting the board.
Almost all systems that use physical computing will have some form of output
What are some examples of Outputs?

## Slide 9: Concepts: INPUT vs. OUTPUT
Referenced from the perspective of the microcontroller (electrical board).
Inputs is a signal / information going into the board.
Output is any signal exiting the board.
Examples: Buttons Switches, Light Sensors, Flex Sensors, Humidity Sensors, Temperature Sensors…
Examples: LEDs, DC motor, servo motor, a piezo buzzer, relay, an RGB LED

## Slide 10: Concepts: Analog vs. Digital
Microcontrollers are digital devices – ON or OFF. Also called – discrete.
analog signals are anything that can be a full range of values. What are some examples? More on this later…
5 V
0 V
5 V
0 V

## Slide 11: Arduino Integrated Development Environment (IDE)
Two required functions / methods / routines:
void setup()
{
// runs once
}
void loop()
{
// repeats
}
error & status messages
Notes: Be sure to point out the what all of the buttons do.

## Slide 12: Settings: Tools  Serial Port
Your computer communicates to the Arduino microcontroller via a serial port  through a USB-Serial adapter.
Check to make sure that the drivers are properly installed.
Notes: All connections to computers- mice, printers etc use a serial port. Gotta pick the right one.

## Slide 13: Settings: Tools  Board
Next, double-check that the proper board is selected under the ToolsBoard menu.
Notes: All connections to computers- mice, printers etc use a serial port. Gotta pick the right one.

## Slide 14
digitalWrite()
analogWrite()
digitalRead()
if() statements / Boolean
analogRead()
Serial communication
This work is licensed under a Creative Commons Attribution-ShareAlike 3.0 United States License.
BIG 6 CONCEPTS

## Slide 15: Let’s get to coding…
Project #1 – Blink
  “Hello World” of Physical Computing
Psuedo-code – how should this work?
Turn LED ON
Wait
Turn LED OFF
Wait
Rinse & Repeat

## Slide 16: Comments, Comments, Comments
Comments are for you – the programmer and your friends…or anyone else human that might read your code.
// this is for single line comments
// it’s good to put a description at the top and before anything ‘tricky’
/* this is for multi-line comments
Like this…
And this….
*/

## Slide 17
comments
Notes: Review the two main parts of the sketch – void setup() and void loop()
Provide rationale for good commenting.
Emphasize the need for good / clean coding practices like indenting.

## Slide 18: Three commands to know…
pinMode(pin, INPUT/OUTPUT);
ex: pinMode(13, OUTPUT);
digitalWrite(pin, HIGH/LOW);
ex: digitalWrite(13, HIGH);
delay(time_ms);
ex: delay(2500); // delay of 2.5 sec.
// NOTE: -> commands are CASE-sensitive
Notes: Three commands to rule the world… or at least do 80% of cool Arduino projects.

## Slide 19: Project #1: Wiring Diagram
Move the green wire from the power bus to pin 13 (or any other Digital I/O pin on the Arduino board.
Image created in Fritzing

## Slide 20: A few simple challenges Let’s make LED#13 blink!
Challenge 1a – blink with a 200 ms second interval.
Challenge 1b – blink to mimic a heartbeat
Challenge 1c – find the fastest blink that the human eye can still detect…
1 ms delay? 2 ms delay? 3 ms delay???

## Slide 21: Try adding other LEDs

## Slide 22: Programming Concepts: Variables
Variable Scope
Global
---
Function-level

## Slide 23: Programming Concepts: Variable Types
Variable Types:
8 bits
16 bits
32 bits
byte
char
int
unsigned int
long
unsigned long
float

## Slide 24
MMorse Code..(use 200ms delay to represent '.' and 700ms delay to represent '-').... Represent 'SOS'

## Slide 25: Exercises to do...before next workshop
Use Morse code to display a message.
Use 2 or more leds to display patterns/disco lights etc.
Read analog input output.
Read Serial input/output.

## Slide 26
Questions?